भारत सरकार /Government of India

उत्तरी क्षेत्र कृषि मशीनरी प्रशिक्षण एवं परीक्षण संस्थान

Northern Region Farm Machinery Training and Testing Institute

ट्रैक्टर नगर, सिरसा रोड, हिसार (हरियाणा)—125001 Tractor Nagar, Sirsa Road, Hisar (Haryana)- 125 001

Website: http://nrfmtti.gov.in   E-mail: fmti-nr@nic.in   GSTIN:06AAAGN0273PIZ3 Tele./FAX: 01662-276984

TECHNICAL SPECIFICATIONS FOR HTP ENGINE OPERATED SPRAYER/ 
ENGINE OPERATED KNAPSACK SPRAYER

| 1 | General: |
| --- | --- |
|  | Name of the machine | : |  |
|  | Type of machine |  |  |
|  | Make | : |  |
|  | Model | : |  |
|  | Serial No. | : |  |
|  | Name of Manufacturer/Importer | : |  |
|  | Name of Applicant | : |  |
|  | Year of manufacture | : |  |
|  | Output capacity, l/min | : |  |
|  | Country of origin | : |  |
| 2 | Prime Mover: |
|  | Name & address of manufacturer | : |  |
|  | Name & address of importer, if any | : |  |
|  | Type | : |  |
|  | Make | : |  |
|  | Model | : |  |
|  | Engine Sr. No. | : |  |
|  | Country of origin | : |  |
|  | Year of manufacture | : |  |
|  | Recommended engine speed Setting, (rpm): |
|  | -Low idle speed | : |  |
|  | -High idle speed | : |  |
|  | Max. power, kW | : |  |
|  | Speed at maximum power, rpm | : |  |
|  | Rated power, kW | : |  |
|  | Rated engine speed, rpm | : |  |
|  | Max. torque, Nm | : |  |
|  | Speed at maximum torque, rpm | : |  |
|  | Whether the prime mover has already been tested by authorized testing centre (Yes/No) | : |  |
|  | If yes, then specify the valid test report No. and upload the copy of test report | : |  |
| 2.1 | Cylinder & Cylinder Head: |
|  | Number | : |  |
|  | Disposition | : |  |
|  | Bore / Stroke, mm | : |  |
|  | Capacity, cc | : |  |
|  | Type of valve | : |  |
|  | Value clearance, mm Inlet Exhaust | : : |  |
|  | Compression ratio | : |  |
| 2.2 | Fuel Supply System: |  |  |
|  | Type of fuel feed | : |  |
| 2.3 | Fuel Tank: |  |  |
|  | Material | : |  |
|  | Capacity of fuel tank, l | : |  |
|  | Location of fuel tank | : |  |
|  | Provision for draining of sediments/ water | : |  |
|  | Fuel filter | : |  |
|  | Fuel on/off | : |  |
| 2.4 | Governor: |  |  |
|  | Make | : |  |
|  | Model | : |  |
|  | Type | : |  |
| 2.5 | Carburetor: |  |  |
|  | Make | : |  |
|  | Type | : |  |
| 2.6 | Fuel injection pump (if applicable): | : |  |
|  | Make | : |  |
|  | Model | : |  |
|  | Serial number/ group combination number | : |  |
| 2.7 | Injector (if applicable): |  |  |
|  | Make | : |  |
|  | Model | : |  |
|  | Type |  |  |
|  | Serial number | : |  |
|  | Number of holes |  |  |
| 2.7 | Air Intake System: |  |  |
|  | Pre cleaner | : |  |
| 2.8 | Air Cleaner: |  |  |
|  | Type | : |  |
|  | Make & Model | : |  |
|  | Location | : |  |
|  | Recommended service schedule | : |  |
|  | Recommended grade of oil | : |  |
| 2.9 | Exhaust: |
|  | Type of silencer | : |  |
|  | Location of silencer | : |  |
|  | Spark arresting device, if any | : |  |
| 2.10 | Lubricant System: |  |  |
|  | Type | : |  |
|  | Oil capacity, l | : |  |
|  | Recommended grade of lubricant oil | : |  |
|  | Oil change period, h | : |  |
| 2.11 | Cooling System: |  |  |
|  | Type | : |  |
|  | Dia. of blower, mm | : |  |
|  | No. of vanes | : |  |
| 2.12 | Starting System: |  |  |
|  | Type | : |  |
|  | Ignition system | : |  |
|  | Any other provision for easy starting | : |  |
|  | Aid for cold starting | : |  |
| 2.13 | Spark plug: |  |  |
|  | Make | : |  |
|  | Model | : |  |
|  | Spark plug electrode gap, mm | : |  |
| 3 | Chemical Tank (if applicable): | : |  |
|  | Material | : |  |
|  | Capacity, l | : |  |
|  | Strainer at filing hole | : |  |
|  | Provision of drain plug in tank | : |  |
|  | Provision of hose reel | : |  |
| 3.1 | Frame (for stationary sprayer): | : |  |
|  | Type | : |  |
|  | Size of angle iron, mm Dia. of pipe, mm | : : |  |
| 3.2 | Agitating Device: |
|  | Type | : |  |
|  | Method of working | : |  |
|  | Method of pressure regulation | : |  |
| 3.4 | Spray Gun: |  |  |
|  | Make | : |  |
| 3.4.1 | Discharge rate at 600 kPa pressure, l/min: |  |  |
|  | -Jet spray pattern | : |  |
|  | -Fine cone spray pattern | : |  |
|  | Spray angle of gun (º) | : |  |
|  | Spray gun designation and marking | : |  |
| 3.5 | Nozzle: |  |  |
|  | Type | : |  |
| 3.5.1 | Discharge rate at 300 kPa pressure, (l/min): |  |  |
|  | Jet spray pattern | : |  |
|  | Fine cone spray pattern | : |  |
|  | Spray angle of nozzle (º) | : |  |
|  | Spray nozzle designation and marking | : |  |
|  | Number of nozzle | : |  |
| 3.6 | Pump: |  |  |
|  | Type | : |  |
|  | Make & model | : |  |
|  | Year of manufacture | : |  |
|  | Serial No. | : |  |
|  | Recommended Pump Speed for spraying, (rpm) | : |  |
|  | Suction volume, l/min |  |  |
|  | Volumetric efficiency, % |  |  |
|  | Working pressure, kg/cm2 | : |  |
|  | Rated pressure, kg/cm2 | : |  |
|  | Pump discharge at rated pressure, l/min |  |  |
|  | Rated speed, rpm | : |  |
|  | Maximum achievable pressure, kg/cm2 | : |  |
|  | Plunger dia./stroke, mm | : |  |
|  | Method of drive | : |  |
|  | Speed reduction from engine to pump | : |  |
|  | Pressure regulator |  |  |
|  | Method of mounting | : |  |
|  | Size of frame, mm: |  |  |
|  | -Length | : |  |
|  | -Width | : |  |
|  | -Height | : |  |
|  | Country of origin | : |  |
| 3.7 | Safety wear (for operator’s safety during operation) | : |  |
| 3.8 | Overall Dimensions, mm: |
|  | Length (without hose) | : |  |
|  | Width | : |  |
|  | Height | : |  |
|  | Length of hose (m), (if applicable) | : |  |
| 4 | Total mass, kg | : |  |
| 4.1 | Mass with all accessories and without fuel, kg | : |  |
| 4.2 | Mass with accessories and fuel tank full, kg | : |  |
| 5 | Details of labeling plate | : |  |

MATERIAL OF CONSTRUCTION OF COMPONENTS OF SPRAYER

[As per Table No.-1of IS: 11313-2007]

| Sr. No. | Components | Materials (As per IS:11313-2007) | Material of the component |
| --- | --- | --- | --- |
| 1. | 2. | 3. | 4. |
| i) | Pump cylinder | Brass, stainless steel |  |
| ii) | Pressure chamber | Brass, stainless steel |  |
| iii) | Piston rod | Stainless steel, |  |
| iv) | Piston or plunger | Gunmetal, stainless steel, plastics, Rubber, vegetable tanned leather, chrome tanned leather |  |
| v) | Spreader | Brass, stainless steel, plastics |  |
| vi) | Valve assembly | Brass, Stainless Steel, Plastics |  |
| vii) | Roller pump shaft | Stainless steel |  |
| viii) | Pump rollers | Nylon filled with lead |  |
| ix) | Pressure regulators | Brass, stainless steel |  |
| x) | Suction strainer | Brass, stainless steel, Plastics |  |
| xi) | Strainer body | Brass, plastics |  |
| xii) | Gasket | Rubber, PVC, fibre, Leather |  |
| xiii) | Spray nozzles | Brass, stainless steel |  |
| xiv) | Spray boom | Mild steel, Galvanized, iron Braided rubber |  |
| xv) | Hose | Synthetic rubber, P.V.C |  |
| xvi) | Tank | Galvanized iron, Brass, Fiber glass reinforced plastics, plastics |  |
| xvii) | Pipe for agitator | Galvanized iron, Brass, PVC |  |
| xviii) | Piston (bucket) screw | Brass, stainless steel |  |
| xix) | Crank case | Aluminum alloy |  |
| xx) | Roller pump body | Nickel resistant cast iron |  |
| xxi) | Roller pump and plate | Nickel resistant cast iron |  |
| xxii) | Roller pump rotor | Nickel resistant cast iron |  |
| xxiii) | Piston pump crank shaft | Carbon steel |  |
| xxiv) | Pump inlet port end fitting | Brass |  |
| xxv) | Piston rod guide | Brass, Aluminum alloy, Gunmetal, Nylon |  |
| xxvi) | Connecting rod | Carbon steel |  |
| xxvii) | Gudgeon pin | Carbon steel |  |
| xxviii) | Big end bearing | Steel coated with tin base white metal |  |
| xxix) | Small end bush | Gunmetal |  |

| Sl. No | Declaration of Engine parameter and Discard limit of Engine Critical Components |
| --- | --- |
| A | Engine parameter: | Declaration |
| i | Recommended engine speed setting, rpm |  |
|  | -Low idle speed |  |
|  | -High idle speed |  |
|  | -Rated speed |  |
| ii | Max. power, kW |  |
| iii | Speed at maximum power, rpm |  |
| iv | Rated power, kW |  |
| v | Specific fuel consumption corresponding to maximum power, kg/kWh |  |
| vi | Maximum equivalent crankshaft torque, Nm |  |
| vii | Speed at maximum torque, rpm: |  |
| viii | Maximum temperatures (ºC): |  |
|  | -Engine oil |  |
|  | -Coolant (water) / liner wall |  |
| ix | Lubricating oil consumption, g/kWh |  |
| x | Coolant consumption (% of total Coolant capacity) (if applicable) |  |
| xi | Smoke level (Bosch No.) |  |
| B | Discard limit of Engine Critical Components: | Discard limit |
| i | Cylinder bore dia., mm |  |
| ii | Piston dia., mm |  |
| iii | Ring-end gap (mm): |  |
|  | -Top compression ring |  |
|  | -2nd compression ring |  |
|  | -3rd compression ring |  |
|  | - Oil ring |  |
| iv | Ring groove clearance (mm): |  |
|  | -Top compression ring |  |
|  | -2nd compression ring |  |
|  | -3rd compression ring |  |
|  | - Oil ring |  |
| v | Clearance of big end bearings (mm): |  |
|  | - Diametrical |  |
|  | - Axial |  |
| vi | Crankshaft end float, mm |  |
| vii | Spring stiffness, kgf/mm |  |
| viii | Valve guide clearance (mm): |  |
|  | -Intake |  |
|  | -Exhaust |  |

Date:

Place:								Signature:

Name of signatory:

Designation:

Name & address of firm: